## Slide 1: Assembly Language for x86 Processors 7th Edition, Global Edition
Chapter 2: x86 Processor Architecture
(c) Pearson Education, 2015. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 1/15/2014 Modified by: Liang, 2016 Spring
Kip Irvine

## Slide 2: Chapter Overview
General Concepts
IA-32 Processor Architecture
  Modes of operation
  Basic execution environment
IA-32 Memory Management
  Protected Mode
64-bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 3: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How program runs

## Slide 4: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 5: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 6: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output
Instruction Execution Cycle

## Slide 7: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  Place the address of the value you want to read on the address bus.
  Assert (changing the value of) the processor’s RD (read) pin.
  Wait one clock cycle for the memory chips to respond.
  Copy the data from the data bus into the destination operand

## Slide 8: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 9: How a Program Runs

## Slide 10: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 11: IA-32 Processor Architecture
Modes of operation
Basic execution environment

## Slide 12: Modes of Operation
Protected mode
  native mode (Windows, Linux)
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 13: Basic Execution Environment
Addressable Memory
General-purpose registers
  Index and base registers
  Specialized register uses
  Status flags
Floating-point, MMX, XMM registers

## Slide 14: General-Purpose Registers
Named storage locations inside the CPU, optimized for speed.
算術邏輯單元 (ALU)
System bus
控制單元 (Control Unit)
暫存器Register
CPU
Memory
EAX | EBP
EBX | ESP
ECX | ESI
EDX | EDI
EIP
EFLAGS
CS
SS
DS
ES
SS
GS
32-bit General-Propose Registers
16-bit Segment
Registers

## Slide 15: Accessing Parts of Registers
Use 8-bit name, 16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX

## Slide 16: Index and Base Registers
Some registers have only a 16-bit name for their lower half:

## Slide 17: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 18: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit

## Slide 19: Status Flags
Carry (bit 0)
  unsigned arithmetic out of range
Overflow (bit 11)
  signed arithmetic out of range
Sign (bit 7)
  result is negative
Zero (bit 6)
  result is zero
Auxiliary Carry (bit 4)
  carry from bit 3 to bit 4
Parity (bit 2)
  sum of 1 bits is an even number
 |  | OF |  | SF | ZF |  | AF |  | PF |  | CF | EFLAGS
31 | … | 11 | … | 7 | 6 | … | 4 | … | 2 | … | 0 | 

## Slide 20: Floating-Point, MMX, XMM Registers
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations

## Slide 21: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 22: IA-32 Memory Management
Real-Address mode
Protected mode

## Slide 23: Real-address mode
linear addresses
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address
Single tasking
Programs can access any area of memory
Notes: 16-bit real mode segment can be overlapped.

## Slide 24: Protected Mode
Designed for multitasking
Each program assigned a memory partition which is protected from other programs
Protected Mode use segment selector’s
1. INDEX is used to get segment descriptor
2. TI is used to decide which kind descriptor table
3. RPL is access right.
Descriptor Table transforms
Logical address into linear address.
And it include base address、
limit and access right.
This access right is used to prevent
program to assign other program’s
Memory address.
Notes: http://godleon.blogspot.tw/2008/02/ia-32-protected-mode-segmentation.html

## Slide 25
INDEX | TI | RPL
ACCESS RIGHTS
LIMIT (00040)
BASE ADDRESS (0000 0000)
DESCRIPTOR TABLE
SEGMENT
DESCRIPTOR
ADDER
SEGMENT SELECTOR
15 3 2 1 0
OFFSET
31 0
31 0
Not used | Physical RAM
FFFFFFFF
00040000
00000000
(4GB)

## Slide 26: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 27: 64-Bit Processors
64-Bit Operation Modes
  Compatibility mode – can run existing 16-bit and 32-bit applications (Windows supports only 32-bit apps in this mode)
  64-bit mode – Windows 64 uses this
Basic Execution Environment
  addresses can be 64 bits (48 bits, in practice)
  16 64-bit general purpose registers
  64-bit instruction pointer named RIP

## Slide 28: 64-Bit General Purpose Registers
32-bit general purpose registers:
  EAX, EBX, ECX, EDX, EDI, ESI, EBP, ESP, R8D, R9D, R10D, R11D, R12D, R13D, R14D, R15D
64-bit general purpose registers:
  RAX, RBX, RCX, RDX, RDI, RSI, RBP, RSP, R8, R9, R10, R11, R12, R13, R14, R15

## Slide 29: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 30: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 31: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 32: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 33: Intel 965 Express Chipset

## Slide 34: Video Output
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required
* This link may change over time.

## Slide 35: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 36: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 37: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 38: Input-Output Ports (cont)
Serial
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 39: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 40: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 41: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 42: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 43: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 44: Summary
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Instruction execution cycle
Multitasking
Floating Point Unit (FPU)
Complex Instruction Set
Real mode and Protected mode
Motherboard components
Memory types
Input/Output and access levels

## Slide 45: 42 69 6E 61 72 79
What does this say?